## Slide 1: Large Pad GEM Beam Test in Hall D @ JLab
Kondo Gnanvo
EIC Weekly Meeting, October 05, 2020

## Slide 2
Principe of large pads readout with high spatial resolution capabilities
Stack of pad layers (5 layers for UVa prototype): 50 µm Kapton with 5 µm Cu pads ⇨ The pad size doubles (area × 4) from one layer to the layer underneath
Pad are arranged in space so that 2 neighboring pads of a given layers always partially share the same area with 2 neighboring pads on the layer underneath
Initial charges shared from one layer to the layer underneath through capacitive coupling (geometrical charge spread)
  Regardless size of bottom layer pads, at least always 2 pads see hits from initial charge cloud hits at least 2 pads of top layer
Only bottom pad layer is read out (readout layer) all the other layers on top participates only on the capacitive coupling charge spread (capacitive layers)
  Spatial resolution performances dictated in first order by the top layer pad size, independent of the bottom pad size
DLC layer on top of the first pad layer is mostly to evacuated the charges from the amplification but could contribute to the initial charge spread
  However DLC charge spread requires pad response function ⇨ so might requires some optimization to minimize its contribution to the charge sharing

## Slide 3
Beam test setup in Hall D @JLab
September 2020
e- (3-6 GeV)
GEM3
GEM2
GEM1
Large Pad GEM
Beam line
Electrons 3-6 GeV
Pair Spectrometer (PS)
gamma
e+
e-
Beam line
Large Pad GEM Telescope
One full week of data with 3 X-Y COMPASS GEM tracker and the large pad GEM
Hall D parasitic beam test with the Pair Spectrometer electron beam (3 to 6 GeV)
Data for HV scan of the large Pad GEM and for spatial resolution studies

## Slide 4
Preliminary results
GEM1
GEM2
Pad GEM
GEM3
y(fit) – y(meas.): min 3-pad cluster
x(fit) – x(meas.): min 3-pad cluster
y(fit) – y(meas.): min 1-pad cluster
x(fit) – x(meas.): min 1-pad cluster
Pad GEM: Response linearity

## Slide 5
Spatial resolution
min 1-pad cluster
σ(X) = 0.49 mm
min 3-pad cluster
σ(X) = 0.47 mm
min 1-pad cluster
σ(X) = 0.43 mm
min 3-pad cluster
σ(X) = 0.41 mm

## Slide 6
Differential non linearity
Differential non linearity plots shows periodic patterns  Could be parameterized for position correction
Additional single pad DNL shown on top plots
DNL is likely caused by 3 sources
  Pad size / resistive layer
  Inter Pad Gap (100 µm)
  Pad traces to the connectors (200 µm)
DNL (y): min 3-pad cluster
DNL (x): min 3-pad cluster
DNL (y): min 1-pad cluster
DNL (x): min 1-pad cluster